## Slide 1: Firewalls
jnlin

## Slide 2: Firewalls
Firewall
  hardware/software
  choke point between secured and unsecured network
  filter incoming and outgoing traffic
  prevent communications which are forbidden by the security policy
What it can be used to do
  Incoming: protect and insulate the applications, services and machines
    Such as telnet, NetBIOS
  Outgoing: limit or disable access from the internal network
    Such as MSN, ssh, ftp, facebook, SC2, D3
  NAT (Network Address Translation)

## Slide 3: Typical Network Design

## Slide 4: Firewalls – Capabilities
Network Layer Firewalls
  Operate at a low level of TCP/IP stack as IP-packet filters.
  Filter attributes
    Source/destination IP
    Source/destination port
    TTL
    Protocols
    …
Application Layer Firewalls
  Work on the application level of the TCP/IP stack.
  Inspect all packets for improper content, a complex work!
Application Firewalls
  The access control implemented by applications.
  TCP Wrapper (libwrap)

## Slide 5: Firewalls – Rules
Exclusive
  Only block the traffic matching the rulesets
Inclusive
  Only allow the traffic matching the rulesets
  Offer much better control of the incoming/outgoing traffic
  Safer than exclusive one
    (Y) reduce the risk of allowing unwanted traffic to pass
    (N) increase the risk to block yourself with wrong configuration
State
  Stateful
    Keep track of which connections are opened through the firewall
    Be vulnerable to Denial of Service (DoS) attacks
  Stateless

## Slide 6: Firewalls – DMZ
Demilitarized zone (Perimeter Network)
  Between untrusted and trusted networks
  Limited access to internal networks
  Open service to WAN (Internet)
    SMTP
    POP3
    HTTP
    VPN Servers
    …
A layer of security
  Limit the damage if system is compromised

## Slide 7: Firewalls – Bastion Host
A workstation allow users connect to internal service
  Limit the entry point of the internal network
  Do logging and auditing on it
  Located in DMZ or behind VPN service

## Slide 8: Firewalls – Packages
Linux
  iptables (kernel 2.4+)
  ipchains (kernel < 2.4)
  Firewalld
  ufw
FreeBSD
  IPFILTER (known as IPF)
  IPFIREWALL (known as IPFW) + Dummynet
  Packet Filter (known as PF)+ ALTQ
    migrated from OpenBSD
    v4.5 (In FreeBSD 9.0)
    http://www.openbsd.org/faq/pf/ v5.0

## Slide 9: iptables in Linux

## Slide 10: iptables
User-space software that control Linux kernel firewall
  Control Linux kernel Netfilter modules
Support kernel version 2.4+
  Replace ipchains and ipfwadm
iptables allows system administrators to define tables containing chains of rules for the treatment of packets

## Slide 11: Packet flow in Netfilter

## Slide 12: Xtables Architecture
Xtables
  v4, v6, arp, eb
  IPv4, IPv6 are different tables
Tables
  filter, nat, mangle
Chains
  PREROUTING, OUTPUT, FORWARD, INPUT, POSTROUTING
Rules
  e.g., iptables -A INPUT -i lo -j ACCEPT

## Slide 13: Xtables Architecture – Filter
Filter Table
  The default table of iptables command
  For packets filter
  INPUT
    Packets that come in (to local)
  OUTPUT
    Packets that go out (from local)
  FORWARD
    Packets that pass through (from others to others)

## Slide 14: Xtables Architecture – NAT
NAT tables
  For IP masquerade
  PREROUTING
    Packets that will go into the routing tables
  POSTROUTING
    Packets that have left the routing tables
  OUTPUT
    Packets that go out (from local)

## Slide 15: Xtables Architecture – Mangle
Mangle Table
  For special purpose, e.g., add or remove some special tags from packets
  PREROUTING
  OUTPUT
  FORWARD
  INPUT
  POSTROUTING

## Slide 16: iptables Flowchart

## Slide 17: iptables – List
iptables
  -t tables : Target table
  -L : List all rules
  -n : Don’t lookup domain names
  -v : Show details

## Slide 18: iptables – Init
iptables
  -F : Flush all rules
  -X : Flush all custom chains
  -Z : Flush all statistics data for all chains
iptables
  -P [INPUT,OUTPUT,FORWARD] [ACCEPT, DROP]
    Change the default policy of the target chain

## Slide 19: iptables – Save and Restore
iptables-restore
  Restore from restore file
iptables-save
  Export all rules and generate restore file
  Some system will load restore file at boot
    Ex: CentOS /etc/sysconfig/iptables /etc/sysconfig/ip6tables
Restore file syntax
  # comments
  * table name
  : chain default-policy [pkt:byte]
  Rules
  COMMIT (End of file)

## Slide 20: iptables – Module
User may need special rule to filter packets
Split several feature into different module
Stateful
  Packets states tracking
  Traffic statistics
Use -m to access module
  iptables -A INPUT -m conntrack …
  iptables -A INPUT -m recent …
http://ipset.netfilter.org/iptables-extensions.man.html

## Slide 21: iptables – Rules (1/2)
Modify
  -A, --append
  -C, --check
  -D, --delete
  -I, --insert
  -R, --replace
Jump
  -j, --jump
    To user-defined chain
    ACCEPT, DROP, REJECT, RETURN, SNAT, DNAT, MASQUERADE
  -g, --goto
    Unlike the --jump option return will not continue processing in this chain but instead in the chain that called us via --jump.

## Slide 22: iptables – Rules (2/2)
Filter
  -i, -o [if] : incoming interface / outgoing interface
    -i ens192 -o docker0
  -s, -d [net] : Source / Destination
    -s 192.168.0.1/24 –d 140.113.1.1
  --sport, --dport [port] : Source port / Destination port
    --sport 22 --dport 80
  -p [protocol] : tcp, udp, icmp, all
    -p icmp
  ! (not) : Invert matching
    ! -s 140.113.1.0/24
    ! -i eth0
    ! -p udp

## Slide 23: iptables – Custom chain
Create
  -N my-chain
  Define in restore file
When iptables reaches the end of user-defined chain, flow returns to the next rule in the calling chain
Ex
  -A INPUT -j badguy
  -A INPUT -j ACCEPT
  -A badguy -s 1.2.3.4 -j DROP
  -A badguy -s 140.112.0.0/24 -j DROP
  …

## Slide 24: Example: Hello world
Allow outgoing packets but deny all incoming packets, except the packets that reply users requests
  -A INPUT -i lo -j ACCEPT
  -A INPUT -m conntrack --ctstate RELATED,ESTABLISHED -j ACCEPT
State
  NEW : New connection
  ESTABLISHED : Old connection
  RELATED : New connection create by ESTABLISHED session
  INVALID

## Slide 25: Example: NAT
Provides NAT from eth0 to eth1
  sysctl -w net.ipv4.ip_forward=1
  -t NAT -A POSTROUTING -i eth0 -o eth1 -j MASQUERADE
Nat
  SNAT --to-source : Change Source IP Address
  DNAT --to-destination : Change Destination IP Address
  MASQUERADE : Change Source IP Address (based on outgoing device IP Address)

## Slide 26: Example: Prevent DDoS Attack
Append traffic limit (10 times / 60 sec) to SSH services
  -A INPUT -p tcp --dport 22 -m state --state NEW -m recent --set --name RECENT --rsource
  -A INPUT -p tcp --dport 22 -m state --state NEW -m recent --rcheck --seconds 60 --hitcount 10 --name RECENT --rsource -j DROP
xt_recent
  Record every connection
  Filter connection by connecting history

## Slide 27: Other tools
These tools help user to manage iptables rules
  UFW (Uncomplicated Firewall) (Ubuntu)
    Easy to use
    Hard to customize
  Firewalld (Redhat)
    Another way to manage your firewall
Sometime even with these tools, you still need to understand iptables, otherwise you cannot manage complicated firewall rules like docker network, kubernetes

## Slide 28: PF in FreeBSD

## Slide 29: Packet Filter (PF)
Functionality
  Filtering packets
  NAT
  Load balance
  QoS: (ALTQ: Alternate Queuing)
  Failover (pfsync + carp)

## Slide 30: PF in FreeBSD – Enable pf*
In /etc/rc.conf (kernel modules loaded automatically)
  pf_enable="YES"
  pflog_enable="YES"
  pfsync_enable="YES"
Kernel configurations
  device pf
  device pflog
  device pfsync

## Slide 31: PF in FreeBSD – Commands
/etc/rc.d/pf
  start / stop / restart / status / check / reload / resync
pfctl
  -e / -d
  -F {nat | rules | state | info | Tables | all | …}
  -v -s {nat | rules | state | info | all | Anchors | Tables | …}
  -v -n -f /etc/pf.conf
  -t <table> -T {add | delete| test} {ip …}
  -t <table> -T {show | kill | flush | …}
  -k {host | network} [-k {host | network}]
  -a {anchor} …
    Default anchor: -a '*'
    Ex. -a ‘ftp-proxy/*’
Notes: start: flush all, and load config
reload: flush everything w/o existing state entries, and load config
restart: stop start
resync: just load config

## Slide 32: PF in FreeBSD – Config ordering
Macros
  user-defined variables, so they can be referenced and changed easily.
Tables “table”
  similar to macros, but efficient and more flexible for many addresses.
Options “set”
  tune the behavior of pf, default values are given.
Normalization “scrub”
  reassemble fragments and resolve or reduce traffic ambiguities.
Queueing “altq”, “queue”
  rule-based bandwidth control.
Translation (NAT) “rdr”, “nat”, “binat”
  specify how addresses are to be mapped or redirected to other addresses
  First match rules
Filtering “antispoof”, “block”, “pass”
  rule-based blocking or passing packets
  Last match rules

## Slide 33: PF in FreeBSD – Lists
Lists
  Allow the specification of multiple similar criteria within a rule
    multiple protocols, port numbers, addresses, etc.
  defined by specifying items within { } brackets.
  eg.
    pass out on rl0 proto { tcp, udp } from { 192.168.0.1, 10.5.32.6 } to any
    pass in on fxp0 proto tcp to port { 22 80 }
  Pitfall
    pass in on fxp0 from { 10.0.0.0/8, !10.1.2.3 }
    You mean (It means) 1. pass in on fxp0 from 10.0.0.0/8 2. block in on fxp0 from 10.1.2.3 2. pass in on fxp0 from !10.1.2.3
    Use table, instead.

## Slide 34: PF in FreeBSD – Macros
Macros
  user-defined variables that can hold IP addresses, port numbers, interface names, etc.
  reduce the complexity of a pf ruleset and also make maintaining a ruleset much easier.
  Naming: start with [a-zA-Z] and may contain [a-zA-Z0-9_]
  eg.
    ext_if = "fxp0“
    block in on $ext_if from any to any
  Macro of macros
    host1 = "192.168.1.1“
    host2 = "192.168.1.2“
    all_hosts = "{" $host1 $host2 "}"

## Slide 35: PF in FreeBSD – Tables (1)
Tables
  used to hold a group of IPv4 and/or IPv6 addresses
    hostname, inteface name, and keyword self
  Lookups against a table are very fast and consume less memory and processor time than lists
  Two attributes
    persist: keep the table in memory even when no rules refer to it
    const: cannot be changed once the table is created
  eg.
    table <private> const { 10/8, 172.16/12, 192.168/16 }
    table <badhosts> persist
    block on fxp0 from { <private>, <badhosts> } to any
    table <spam> persist file "/etc/spammers" file "/etc/openrelays"

## Slide 36: PF in FreeBSD – Tables (2)
Tables – Address Matching
  An address lookup against a table will return the most narrowly matching entry
  eg.
    table <goodguys> { 172.16.0.0/16, !172.16.1.0/24, 172.16.1.100 }
    block in on dc0
    pass in on dc0 from <goodguys>
  Result
    172.16.50.5 passed
    172.16.1.25 blocked
    172.16.1.100 passed
    10.1.4.55 blocked

## Slide 37: PF in FreeBSD – Options
Format
  control pf's operation, and specified in pf.conf using “set”
    Format: set option [sub-ops] value
Options
  loginterface – collect packets and gather byte count statistics
  ruleset-optimization – ruleset optimizer
    none, basic, profile
    basic: remove dups, remove subs, combine into a table, re-order rules
  block-policy – default behavior for blocked packets
    drop, return
  skip on {ifname} – interfaces for which packets should not be filtered.
    eg. set skip on lo0
  timeout, limit, optimization, state-policy, hostid, require-order, fingerprints, debug

## Slide 38: PF in FreeBSD – Normalization
Traffic Normalization
  IP fragment reassembly
    scrub in all
  Default behavior
    Fragments are buffered until they form a complete packet, and only the completed packet is passed on to the filter.
    Advantage: filter rules have to deal only with complete packets, and ignore fragments.
    Disadvantage: caching fragments is the additional memory cost
    The full reassembly method is the only method that currently works with NAT.

## Slide 39: PF in FreeBSD – Translation (1)
Translation
  Modify either the source or destination address of the packets
  The translation engine
    modifies the specified address and/or port in the packet
    passes it to the packet filter for evaluation
  Filter rules filter based on the translated address and port number
  Packets passed directly if the pass modifier is given in the rule

## Slide 40: PF in FreeBSD – Translation (2)
Various types of translation
  binat – bidirectional mapping between an external IP netblock and an internal IP netblock
    binat on $ext_if from 10.1.2.150 to any -> 140.113.235.123
    binat on $ext_if from 192.168.1.0/28 to any -> 140.113.24.0/28
  nat – IP addresses are to be changes as the packet traverses the given interface
    no nat on $ext_if from 192.168.123.234 to any
    nat pass on $ext_if from 192.168.123.0/24 to any -> 140.113.235.21
  rdr – redirect packets to another destination and possibly different port
    no rdr on $int_if proto tcp from any to $server port 80
    rdr on $int_if proto tcp from any to any port 80 -> 127.0.0.1 port 80
Notes: Port range rdr

## Slide 41: PF in FreeBSD – Translation (3)
Evaluation
  Evaluation order of translation rules depends on the type
    binat rules first, and then either rdr rules for inbound packets or nat rules for outbound packets
  Rules of the same type are evaluated in the order of appearing in the ruleset
  The first matching rule decides what action is taken
  If no rule matches the packet, it is passed to the filter unmodified

## Slide 42: PF in FreeBSD – Packet Filtering (1)
pf has the ability to block and pass packets based on
  layer 3(ip, ip6) and layer 4(icmp, icmp6, tcp, udp) headers
Each packet processed by the filter
  The filter rules are evaluated in sequential order
  The last matching rule decides what action is taken
  If no rule matches the packet, the default action is to pass
Format
  {pass | block [drop | return]} [in | out] [log] [quick] [on ifname] … {hosts} …
  The simplest to block everything by default: specify the first filter rule
    block all

## Slide 43: PF in FreeBSD – Packet Filtering (2)
States
  If the packet is passed, state is created unless the no state is specified
    The first time a packet matches pass, a state entry is created
    For subsequent packets, the filter checks whether each matches any state
    For TCP, also check its sequence numbers
    pf knows how to match ICMP replies to states
      Port unreachable for UDP
      ICMP echo reply for echo request
      …
    Stores in BST for efficiency

## Slide 44: PF in FreeBSD – Packet Filtering (3)
Parameters
  in | out – apply to imcoming or outgoing packets
  log - generate log messages to pflog (pflog0, /var/log/pflog)
    Default: the packet that establishes the state is logged
  quick – the rule is considered the last matching rule
  on ifname – apply only on the particular interface
  inet | inet6 – apply only on this address family
  proto {tcp | udp | icmp | icmp6} – apply only on this protocol

## Slide 45: PF in FreeBSD – Packet Filtering (4)
Parameters
  hosts : { from host [ port [op] # ] to host [port [op] #] | all }
  host:
    host can be specified in CIDR notation, hostnames, interface names, table, or keywords any, self, …
    Hostnames are translated to address(es) at ruleset load time.
    When the address of an interface or hostname changes, the ruleset must be reloaded
    When interface name is surrounded by (), the rule is automatically updated whenever the interface changes its address
  port:
    ops: unary(=, !=, <, <=, >, >=), and binary(:, ><, <>)
  eg.
    block in all
    pass in proto tcp from any port < 1024 to self port 33333:44444

## Slide 46: PF in FreeBSD – Packet Filtering (5)
Parameters
  flags {<a>/<b> | any} – only apply to TCP packets
    Flags: (F)IN, (S)YN, (R)ST, (P)USH, (A)CK, (U)RG, (E)CE, C(W)R
    Check flags listed in <b>, and see if the flags (not) in <a> is (not) set
    eg.
      flags S/S : check SYN is set, ignore others.
      flags S/SA: check SYN is set and ACK is unset., ignore others
    Default flags S/SA for TCP
  icmp-type type code code
  icmp6-type type code code
    Apply to ICMP and ICMP6 packets
  label – for per-rule statistics
  {tag | tagged} string
    tag by nat, rdr, or binat, and identify by filter rules.

## Slide 47: PF in FreeBSD – Load Balance
Load balance
  For nat and rdr rules
  eg.
    rdr on $ext_if proto tcp from any to any port 80 \ -> {10.1.2.155, 10.1.2.160, 10.1.2.161} round-robin

## Slide 48: PF in FreeBSD – Security
For security consideration
  state modulation
    Create a high quality random sequence number
    Applying modulate state parameter to a TCP connection
  syn proxy
    pf itself completes the handshake
    Applying synproxy state parameter to a TCP connection
      Include modulate state

## Slide 49: PF in FreeBSD – Stateful tracking
Stateful tracking options
  keep state, modulate state, and synproxy state support these options
    keep state must be specidied explicitly to apply options to a rule
  eg.
    table <bad_hosts> persist
    block quick from <bad_hosts>
    pass in on $ext_if proto tcp to ($ext_if) port ssh keep state \ ( max-src-conn-rate 5/30, overload <bad_hosts> flush global)

## Slide 50: PF in FreeBSD – Blocking spoofed
Blocking spoofed traffic
  antispoof for ifname
  antispoof for lo0
    block drop in on ! lo0 inet from 127.0.0.1/8 to any
    block drop in on ! lo0 inet6 from ::1 to any
  antispoof for wi0 inet (IP: 10.0.0.1, netmask 255.255.255.0)
    block drop in on ! wi0 inet from 10.0.0.0/24 to any
    block drop in inet from 10.0.0.1 to any
  Pitfall:
    Rules created by the antispoof interfere with packets sent over loopback interfaces to local addresses. One should pass these explicitly.
    set skip on lo0

## Slide 51: PF in FreeBSD – Anchors
Besides the main ruleset, pf can load rulesets into anchor attachment points
  An anchor is a container that can hold rules, address tables, and other anchors
  The main ruleset is actually the default anchor
  An anchor can reference another anchor attachment point using
    nat-anchor
    rdr-anchor
    binat-anchor
    anchor
    load anchor <name> from <file>

## Slide 52: PF in FreeBSD – Example
Ex.
# macro definitions
extdev='fxp0‘
server_ext=‘140.113.214.13’
# options
set limit { states 10000, frags 5000 }
set loginterface $extdev
set block-policy drop
set skip on lo0
# tables
table <badhosts> persist file “/etc/badhosts.list”
# filtering rules
block in all
pass out all
antispoof for $extdev
block log in on $extdev proto tcp from any to any port {139, 445}
block log in on $extdev proto udp from any to any port {137, 138}
block on $extdev quick from <badhosts> to any
pass in on $extdev proto tcp from 140.113.0.0/16 to any port {139, 445}
pass in on $extdev proto udp from 140.113.0.0/16 to any port {137, 138}

## Slide 53: PF in FreeBSD – Debug by pflog
Enable pflog in /etc/rc.conf (pflog.ko loaded automatically)
  pflog_enable="YES"
    Log to pflog0 interface
    tcpdump -i pflog0
  pflog_logfile="/var/log/pflog"
    tcpdump -r /var/log/pflog
Create firewall rules
  Default configuration rules
    pf_rules="/etc/pf.conf"
  Sample files
    /usr/share/examples/pf/*

## Slide 54: NAT on FreeBSD (1)
Setup
  Network topology
  configuration
  Advanced redirection configuration
192.168.1.1
Web server
192.168.1.2
Ftp Server
192.168.1.101
PC1

## Slide 55: NAT on FreeBSD (2)
In /etc/rc.conf
  ifconfig_fxp0="inet 140.113.235.4"
  ifconfig_fxp1="inet 192.168.1.254/24"
  defaultrouter="140.113.235.254"
  gateway_enable="YES"
In /etc/pf.conf
  nat
  rdr
  binat
# macro definitions
extdev='fxp0‘
intranet='192.168.1.0/24‘
webserver=‘192.168.1.1’
ftpserver=‘192.168.1.2’
winxp=‘192.168.1.101’
server_int=‘192.168.1.88’
server_ext=‘140.113.235.13’
# nat rules
nat on $extdev inet from $intranet to any -> $extdev
rdr on $extdev inet proto tcp to port 80 -> $webserver port 80
rdr on $extdev inet proto tcp to port 443 -> $webserver port 443
rdr on $extdev inet proto tcp to port 21 -> $ftpserver port 21
rdr on $extdev inet proto tcp to port 3389 -> $winxp port 3389
binat on $extdev inet from $server_int to any -> $server_ext
Notes: gateway_enable="YES"

## Slide 56: ALTQ: Alternate Queue – (1)
Rebuild Kernel is needed
  http://www.freebsd.org/doc/handbook/firewalls-pf.html
  ALTQ related kernel options and supported devices
    man 4 altq
  ipchains

## Slide 57: ALTQ: Alternate Queue – (2)
altq on dc0 cbq bandwidth 5Mb queue {std, http}
queue std bandwidth 10% cbq(default)
queue http bandwidth 60% priority 2 cbq(borrow) {employee,developer}
queue developers bandwidth 75% cbq(borrow)
queue employees bandwidth 15%
block return out on dc0 inet all queue std
pass out on dc0 inet proto tcp from $developerhosts to any port 80 queue developers
pass out on dc0 inet proto tcp from $employeehosts to any port 80 queue employees
pass out on dc0 inet proto tcp from any to any port 22
pass out on dc0 inet proto tcp from any to any port 25