## Slide 1: SNMP
Simple Network Management Protocol
wangth

## Slide 2: Network Management
The network management is to
  Monitor the network
  Ensure the operations over the network are functional
  Assure the network works efficiently
An ounce of prevention is worth a pound of cure
  Something wrong
    Service down, fix the problem, resume the service
  Nothing wrong
    Service is somewhat abnormal, try to fix it online
Requirements
  FCAPS

## Slide 3: Requirements of Network Management
Fault Management
  Detect, isolate, reconfigurate and repair the abnormal network environment
  Problem tracking and control
Configuration Management
  Gather configuration information of network components
Accounting Management
  Track the use of network resources by end-user to provide
    Impropriate usage tracing, charging, statistics
Performance Management
  Capacity utilization, throughput, response time, bottleneck
    Collect information and assess current situation
Security Management
  Information protection and access control

## Slide 4: In that time
Network environment is simple
  ICMP is the only way to do network investigation
    ping, traceroute, ….
As Internet goes popular, three approaches are proposed:
  HEMS: High-level Entity Management System
    Considered to be the first network management tools
  SGMP and SNMP
    SNMP was an enhanced version of the Simple Gateway Management Protocol
    For TCP/IP-based network management standards
    Supposed to be short-term solution
  CMIP over TCP/IP (CMOT)
    Common Management Information Protocol
    For ISO-based network management standards
    Supposed to be long-term solution

## Slide 5: Introduction
SNMP – Simple Network Management Protocol
  A set of standards for network management
    Protocol
    Database structure specification
    Data objects
  A set of standardized tools that
    Control costs of network management
    Across various product types
      End system, bridges, routers, telecommunications, …
  Two roles
    Network management station: SNMP collector, manager
    SNMP agent

## Slide 6: History
In 1989
  SNMP was adopted as TCP/IP-based Internet standards
In 1991
  RMON – Remote network MONitoring
    Supplement to SNMP to include management of LAN and WAN packet flow
In 1995
  SNMPv2 (2c)
    Functional enhancements to SNMP
    SNMP on OSI-based networks
  RMON2
    Network layer and application layer
In 1998
  SNMPv3
    Precise definition, but the content is the same as SNMPv2
    Security capability for SNMP

## Slide 7: The roles in SNMPv3
Notes: http://www.tml.tkk.fi/Opinnot/Tik-110.551/1999/papers/12ManagementOfIPngCore/ipcore.html

## Slide 8: Network Management System (1)
A collection of tools for
  Network monitoring
  Network control
These tools must be integrated
  Single operator interface with powerful but user-friendly
  Support of managed equipment

## Slide 9: Network Management System (2)
Architecture of NMS
  NMA
    Operator interface
  NME
    Collect statistics
    Response to NMA
    Alert NMA when environment changing

## Slide 10: SNMP Concepts

## Slide 11: SNMP Architecture (1)
4 key elements
  Management Station
    Serve as the interface between manager and devices
      Management applications
      User-friendly interface
      Translate manager’s requirements into actual monitoring or control operations
      Database extracted from MIBs of all managed device
  Management Agent
    Respond to request from management station
    Change settings in MIB of managed device
    Asynchronously report abnormal event (Trap)
  Management Information Base (MIB)
    Each resource is represented as an object and MIB is a collection of objects
  Network Management Protocol
    get, setnext, set, getresponse, trap, ...

## Slide 12: SNMP Architecture (2)
SNMP
  UDP
  Port 161(snmp)
  Port 162(snmp-trap)

## Slide 13: SNMP Architecture (3)
SNMP proxy
  Devices that do not support UDP/IP
    e.g., Bridge, Modem
  Devices that do not want to add burden of SNMP agent
    e.g., PC, programmable controller

## Slide 14: SNMP Management Information
Management Information Base (MIB)
  Collection of objects
  Each object represents certain resource of managed device
Interoperability of MIB
  Object that represents a particular resource should be the same cross various system
    What objects
    (MIB-I) and MIB-II
  Common representation format
    SMI (Structure of Management Information)

## Slide 15: SNMP Management Information – SMI (1)
SMI
  Structure of Management Information
  Identify the data type that can be used in MIB
  How resources are represented and named, including
    MIB structure
    Syntax and value of each object
    Encoding of object value

## Slide 16: SNMP Management Information – SMI (2)
MIB structure
  Rooted tree
    The leaves are the actual managed objects
    Each object has an identifier (OBJECT IDENTIFIER)
      Number with dot as delimiter
    The internet node
      iso(1) -> org(3) -> dod(6) -> internet(1)
      object identifier of internet node: 1.3.6.1
    Under internet node
      directory(1) :OSI X.500 directory
      mgmt(2): used for objects defined in IAB (Internet Activities Board)
      experimental(3): used for internet experiments
      private(4): unilaterally usage

## Slide 17: SNMP Management Information – SMI (3)
  MIB Tree
  Define additional objects
    Under mib-2
      1.3.6.1.2.1
    Under experimental
      1.3.6.1.3
    Under enterprises
      1.3.6.1.4.1

## Slide 18: SNMP Management Information – Object Syntax (1)
Definition of object
  Data type
    Application-independent type (UNIVERSAL type)
      Integer, Octet String, Object Identifier, Null, Sequence, Sequence Of
    Application-wide types (RFC 1155)
      NetworkAddress  Not used
      IpAddress
      Counter (0 ~ 232 -1), increasing only, wrap to 0
      Gauge (0 ~ 232 -1)
      TimeTicks
      Opaque (encoded as OCTET STRING for transmission)
  Value ranges
  Relationship with other objects in MIB

## Slide 19: SNMP Management Information – Object Syntax (2)
ASN.1
  Abstract Syntax Notation One
  A formal language developed by CCITT and ISO
  In SNMP, we use macro to define other types used to define managed objects
    Macro definition (template)
    Macro instance (particular type)
    Macro instance value

## Slide 20: SNMP Management Information – Object Syntax (3)
Example: /usr/share/snmp/mibs/BEGEMOT-HOSTRES-MIB.txt
-- Additional stuff for the HOST-RESOURCES MIB.
BEGEMOT-HOSTRES-MIB DEFINITIONS ::= BEGIN
IMPORTS
MODULE-IDENTITY, OBJECT-TYPE, TimeTicks
FROM SNMPv2-SMI
begemot
FROM BEGEMOT-MIB;
begemotHostres MODULE-IDENTITY
….
::= { begemot 202 }
begemotHostresObjects OBJECT IDENTIFIER ::= { begemotHostres 1 }
begemotHrStorageUpdate OBJECT-TYPE
SYNTAX TimeTicks
MAX-ACCESS read-write
STATUS current
DESCRIPTION
"The maximum number of ticks the storage table is cached."
::= { begemotHostresObjects 1 }

## Slide 21: SNMP Management Information – Object Syntax (4)
OBJECT-Type macro

## Slide 22: SNMP Management Information – Object Syntax (5)
Example of object definition
  iso.org.dod.internet.mgmt.mib-2.tcp.tcpMaxConn
  1.3.6.1.2.1.6.4

## Slide 23: SNMP Management Information – Object Syntax (6)
2-D table
  Two-dimensional array with scalar-valued entries
  Ex: tcpConnTable (RFC1213)

## Slide 24: SNMP Management Information – Object Syntax (7)

## Slide 25: SNMP Management Information – Object Syntax (8)
  iso (1) -> org (3) -> dod (6) -> internet (1) -> mgmt (2)
    mib-2 (1) -> tcp (6) -> tcpConnTable(13)

## Slide 26: Standard MIBs

## Slide 27: MIB-II (1)
RFC1213
  MIB-I (RFC 1156)
  MIB-II is a superset of MIB-I with some additional objects and groups

## Slide 28: MIB-II (2)
First layer under mib-2
  1.3.6.1.2.1 (iso.org.dod.internet.mgmt.mib-2)
  system
    Overall information about the system
  interfaces
    Information about each interface
  at
    Address translation (obsolete)
  ip, icmp, tcp, udp, egp
  transmission
    Transmission schemes and access protocol at each system interface
  snmp

## Slide 29: MIB-II system group
sysServices
  1 physical (ex: repeater)
  2 datalink/subnetwork (ex: bridge)
  3 internet (ex: router)
  4 end-to-end (ex: IP hosts)
  7 applications (ex: mail relays)

## Slide 30: MIB-II interface group (1)

## Slide 31: MIB-II interface group (2)

## Slide 32: MIB-II tcp group

## Slide 33: MIB-II ip group

## Slide 34: Host Resources MIB
RFC2790
  host OBJECT IDENTIFIER ::= { mib-2 25 }
  hrSystem OBJECT IDENTIFIER ::= { host 1 }
  hrStorage OBJECT IDENTIFIER ::= { host 2 }
  hrDevice OBJECT IDENTIFIER ::= { host 3 }
  hrSWRun OBJECT IDENTIFIER ::= { host 4 }
  hrSWRunPerf OBJECT IDENTIFIER ::= { host 5 }
  hrSWInstalled OBJECT IDENTIFIER ::= { host 6 }
  hrMIBAdminInfo OBJECT IDENTIFIER ::= { host 7 }

## Slide 35: SNMP Protocol

## Slide 36: SNMP Protocol
Supported operations
  get, getnext, set, getresponse, trap, …
Simplicity vs. limitations
  Not possible to change the structure of MIB by adding or deleting object instances
  Access is provided only to leaf objects

## Slide 37: SNMP Protocol – security concern
In management environment
  The management station and managed agent
    One-to-many relationship
    One station may manage all or a subset of target
  The managed agent and management station
    One-to-many relationship
    Each managed agent controls its local MIB and must be able to control the use of that MIB
    Three aspects
      Authentication service
      Access policy
      Proxy service

## Slide 38: SNMP Protocol – communities (1)
An SNMP community
  A relationship between an SNMP agent and a set of SNMP managers that defines
    Authentication, access control and proxy
  The managed system establishes one community for each combination of authentication, access control and proxy
  Each community has a unique “community name”
  Management station use certain community name in all get and set operations

## Slide 39: SNMP Protocol – communities (2)
Authentication
  The community name (password)
Access policy
  Community profile
    SNMP MIB view
      A subset of MIB objects
    SNMP access mode
      read-only, read-write, write-only, non-accessible

## Slide 40: SNMP Protocol – Where is the security
SNMPv3
  User-based Security Model (USM)
    Message Authentication
      HMAC
        MD5, SHA-1
        Authentication passphrase, secret key
    Encryption
      CBC-DES
  View-based Access Control Model (VACM)
    Context table
    Security to group table
    Access table
    View tree family table

## Slide 41: BSNMP
mini SNMP daemon

## Slide 42: BSNMP (1)
A portable SNMP framework consisting of a daemon (bsnmpd), modules and tools
Enable bsnmpd
  /etc/rc.conf
Configure bsnmpd
  /etc/snmpd.config
Start bsnmpd
  /etc/rc.d/bsnmpd start
  Firewall allows
    snmpd: udp 161
    snmptrapd: udp 162
bsnmpd_enable="YES"
location := "Room 200"
contact := "sysmeister@example.com"
system := 1 # FreeBSD
traphost := localhost
trapport := 162
# Change this!
read := "public“
# Host resources module
# This requires the mibII module.
#
#begemotSnmpdModulePath."hostres" = "/usr/lib/snmp_hostres.so"

## Slide 43: BSNMP (2)
bsnmp-ucd
  bsnmpd module that implements parts of UCD-SNMP-MIB
  The counters will be available under the following MIB: .1.3.6.1.4.1.2021 (UCD-SNMP-MIB::ucdavis)
Install bsnmp-ucd
  net-mgmt/bsnmp-ucd
Configure bsnmpd
  /etc/snmpd.config
Restart bsnmpd
Other bsnmp modules
  bsnmp-jails
    bsnmpd module to measure statistics about jails
  bsnmp-regex
    bsnmpd module allowing creation of counters from log files
begemotSnmpdModulePath."ucd" = "/usr/local/lib/snmp_ucd.so"

## Slide 44: Net-SNMP
previously known as "ucd-snmp"

## Slide 45: Net-SNMP (1)
Install net-snmp
  net-mgmt/net-snmp
  # make [OPTIONS] install clean
  Firewall allows
    snmpd: udp 161
    snmptrapd: udp 162
DEFAULT_SNMP_VERSION="3" Default version of SNMP to use.
NET_SNMP_SYS_CONTACT="nobody@nowhere.invalid"
Default system contact.
NET_SNMP_SYS_LOCATION="somewhere"
Default system location.
NET_SNMP_LOGFILE="/var/log/snmpd.log"
Default log file location for snmpd.
NET_SNMP_PERSISTENTDIR="/var/net-snmp"
Default directory for persistent data storage.

## Slide 46: Net-SNMP (2)
After installing…
  /usr/local/share/snmp/snmpd.conf.example
If you want to auto-start snmpd and snmptrapd:, add the following to
/etc/rc.conf:
snmpd_enable="YES"
snmpd_flags="-a"
snmpd_conffile="/usr/local/share/snmp/snmpd.conf /etc/snmpd.conf"
snmptrapd_enable="YES"
snmptrapd_flags="-a -p /var/run/snmptrapd.pid"
# Full access from the local host
# rocommunity public localhost
# Default access to basic system info
rocommunity public default -V systemonly

## Slide 47: Net-SNMP (3)
Use snmpconf command to generate the configuration files
  snmpconf -g basic_setup
  snmpconf
    System Information Setup
      Location, contact, service
    Access Control Setup
      SNMPv3 or SNMPv1 access community
    Trap Destination
      Where to send the trap
    Monitor Various Aspects of the Running Host
      Process, disk space, load, file
    Extending the Agent
      Let snmp agent to return information that yourself define
    Agent Operating Mode
      User/group, IP port,…

## Slide 48: Net-SNMP (4)
To get various value
  man snmpget, snmpgetnext, snmptable
    % snmpget -c public -v 1 nasa system.sysContact.0
    % snmpgetnext -c public –v 1 nasa system.sysContact.0
    % snmptable -c public -v 1 nasa mib-2.tcp.tcpConnTable
    % snmpwalk -c public -v 1 nasa system
    % snmpwalk -c public -v 1 nasa iso.org.dod.internet.private.enterprises

## Slide 49: Appendix
Cacti

## Slide 50: Cacti(1)
About
  Cacti is a complete network graphing solution designed to harness the power of RRDTool's data storage and graphing functionality.
  Cacti provides a fast poller, advanced graph templating, multiple data acquisition methods, and user management features out of the box.
  All of this is wrapped in an intuitive, easy to use interface that makes sense for LAN-sized installations up to complex networks with hundreds of devices.
Install cacti
  /usr/ports/net/cacti

## Slide 51: Cacti(2)

## Slide 52: Cacti(3)

## Slide 53: Cacti(4)

## Slide 54: Cacti(5)
Default account/pwd
  admin/admin

## Slide 55: Cacti(6)

## Slide 56: Cacti(7)