## Slide 1: Routing

## Slide 2
Dynamic Route
Routing Protocol

## Slide 3: Why dynamic route ? (1)
Static route is ok only when
  Network is small
  There is a single connection point to other network
  No redundant route

## Slide 4: Why dynamic route ? (2)
Dynamic Routing
  Routers update their routing table with the information of adjacent routers
  Dynamic routing need a routing protocol for such communication
  Advantage:
    They can react and adapt to changing network condition

## Slide 5: Routing Protocol
Used to change the routing table according to various routing information
  Specify detail of communication between routers
  Specify information changed in each communication,
    Network reachability
    Network state
    Metric
Metric
  A measure of how good a particular route
    Hop count, bandwidth, delay, load, reliability, …
Each routing protocol may use different metric and exchange different information

## Slide 6: Autonomous System
Autonomous System (AS)
  Internet is organized into a collection of autonomous system
  An AS is a collection of networks with same routing policy
    Single routing protocol
    Normally administered by a single entity
      Corporation or university campus
    All depend on how you want to manage routing

## Slide 7: Category of Routing Protocols – by AS
AS-AS communication
  Communications between routers in different AS
  Interdomain routing protocols
  Exterior gateway protocols (EGP)
  Ex:
    BGP (Border Gateway Protocol)
Inside AS communication
  Communication between routers in the same AS
  Intradomain routing protocols
  Interior gateway protocols (IGP)
  Ex:
    RIP (Routing Information Protocol)
    IGRP (Interior Gateway Routing Protocol)
    OSPF (Open Shortest Path First Protocol)

## Slide 8: Intra-AS and Inter-AS routing
Host
h2
a
b
b
a
a
C
A
B
d
c
A.a
A.c
C.b
B.a
c
b
Host
h1
Intra-AS routing
within AS A
Inter-AS
routing
between
A and B
Intra-AS routing
within AS B
inter-AS, intra-AS routing in
gateway A.c
network layer
link layer
physical layer

## Slide 9: Category of Routing Protocols – by information changed (1)
Distance-Vector Protocol
  Message contains a vector of distances, which is the cost to other network
  Each router updates its routing table based on these messages received from neighbors
  Protocols:
    RIP
    IGRP
    BGP

## Slide 10: Category of Routing Protocols – by information changed (2)
Link-State Protocol
  Broadcast their link state to neighbors and build a complete network map at each router using Dijkstra algorithm
  Protocols:
    OSPF

## Slide 11: Difference between Distance-Vector and Link-State
Difference
Information update sequence
Distance-Vector
Link-State
 | Distance-Vector | Link-State
Update | updates neighbor (propagate new info.) | update all nodes
Convergence | Propagation delay cause slow convergence | Fast convergence
Complexity | simple | Complex

## Slide 12: Routing Protocols
        RIP IGP,DV IGRP IGP,DV OSPF IGP,LS BGP EGP

## Slide 13: RIP
RIP
  Routing Information Protocol
Category
  Interior routing protocol
  Distance-vector routing protocol
    Using “hop-count” as the cost metric
Example of how RIP advertisements work
Routing table in router before
Receiving advertisement
Advertisement from router A
Routing table after
receiving advertisement
Destination network | Next router | # of hops to destination
1 | A | 2
20 | B | 2
30 | B | 7
Destination network | Next router | # of hops to destination
30 | C | 4
1 | -- | 1
10 | -- | 1
Destination network | Next router | # of hops to destination
1 | A | 2
20 | B | 2
30 | A | 5

## Slide 14: RIP – Example
Another example

## Slide 15: RIP – Message Format
RIP message is carried in UDP datagram
  Command: 1 for request and 2 for reply
  Version: 1 or 2 (RIP-2)
20 bytes per
route entry

## Slide 16: RIP – Operation
routed – RIP routing daemon
  Operated in UDP port 520
Operation
  Initialization
    Probe each interface
    send a request packet out each interface, asking for other router’s complete routing table
  Request received
    Send the entire routing table to the requestor
  Response received
    Add, modify, delete to update routing table
  Regular routing updates
    Router sends out their routing table to every neighbor every 30 minutes
  Triggered updates
    Whenever a route entry’s metric change, send out those changed part routing table

## Slide 17: RIP – Problems of RIP
Issues
  15 hop-count limits
  Take long time to stabilize after the failure of a router or link
  No CIDR
RIP-2
  EGP support
    AS number
  CIDR support

## Slide 18: IGRP (1)
IGRP – Interior Gateway Routing Protocol
Similar to RIP
  Interior routing protocol
  Distance-vector routing protocol
Difference between RIP
  Complex cost metric other than hop count
    delay time, bandwidth, load, reliability
    The formula
  Use TCP to communicate routing information
  Cisco System’s proprietary routing protocol
Notes: 和IRP不同的地方在不再只有找最短路徑
會考量更多

## Slide 19: IGRP (2)
Advantage over RIP
  Control over metrics
Disadvantage
  Still classful and has propagation delay
  Vendor dependency
Notes: IGRP有支援lowbbalence
最多可支援六個

## Slide 20: OSPF (1)
OSPF
  Open Shortest Path First
Category
  Interior routing protocol
  Link-State protocol
Each interface is associated with a cost
  Generally assigned manually
  The sum of all costs along a path is the metric for that path
Neighbor information is broadcast to all routers
  Each router will construct a map of network topology
  Each router run Dijkstra algorithm to construct the shortest path tree to each routers

## Slide 21: OSPF – Dijkstra Algorithm
Single Source Shortest Path Problem
  Dijkstra algorithm use “greedy” strategy
  Ex:

## Slide 22: OSPF – Routing table update example (1)

## Slide 23: OSPF – Routing table update example (2)

## Slide 24: OSPF – Summary
Advantage
  Fast convergence
  CIDR support
  Multiple routing table entries for single destination, each for one type-of-service
    Load balancing when cost are equal among several routes
Disadvantage
  Large computation
Notes: 可快速收斂
CIDR有支援
可紀錄多個路徑
缺:需要跑演算法

## Slide 25: ISIS (1)
ISIS
  Intermediate System to Intermediate System
Category
  Interior routing protocol
  Link-State protocol
Each interface is associated with a cost
  Generally assigned manually
  The sum of all costs along a path is the metric for that path
Neighbor information is broadcast to all routers
  Each router run Dijkstra algorithm to construct the shortest path tree to each routers
Rides directly above layer two
  I/IS-IS runs on top of the Data Link Layer

## Slide 26: Comparing ISIS and OSPF (1)
Same
  Interior routing protocol (IGP)
  Link-State protocol
  Classless Inter-Domain Routing (CIDR)
  Variable Subnet Length Masking (VLSM)
  Authentication
  Multi-path
  IP unnumbered links

## Slide 27: Comparing ISIS and OSPF (2)
OSPF
  Host
  Router
  Link
  Packet
  Designated Router (DR)
  Backup DR (BDR)
  Link-Stats Advertisement (LSA)
  Hello packet
  Database Description(DBD)
ISIS
  End System(ES)
  Intermediate System(IS)
  Circuit
  Protocol Data Unit (PDU)
  Designated IS (DIS)
  N/A
  Link-State PDU (LSP)
  IIH PDU
  Complete sequence number PDU (CSNP)

## Slide 28: Comparing ISIS and OSPF (3)
OSPF
  Area
  Non-backbone area
  Backbone area
  Area Border Router(ABR)
  Autonomous System Boundary Router (ASBR)
ISIS
  Sub domain (area)
  Level-1 area
  Level-2 Sub domain (backbone)
  L1L2 router
  Any IS

## Slide 29: BGP (1)
BGP
  Border Gateway Protocol
Exterior routing protocol
  Now BGP-4
  Exchange network reachability information with other BGP systems
Routing information exchange
  Message:
    Full path of autonomous systems that traffic must transit to reach destination
    Can maintain multiple route for a single destination
  Exchange method
    Using TCP
    Initial: entire routing table
    Subsequent update: only sent when necessary
    Advertise only optimal path
Route selection
  Shortest AS path
Notes: 和IGP不同的地方是
BGP必須要非常明白的說明所走的路徑

## Slide 30: BGP (2)
Incremental Updates
Many options for policy enforcement
Classless Inter Domain Routing (CIDR)
Widely used for Internet backbone
Autonomous systems
140.113.0.0/16 *[BGP/170] 1w1d 02:30:41, localpref 200, from 62.115.128.39 AS path: 9505 18185 9916 I
https://nsrc.org/workshops/2016/senix-ixp/presentations/00-BGP-Introduction.pdf
Notes: 和IGP不同的地方是
BGP必須要非常明白的說明所走的路徑

## Slide 31: Routing Protocols Comparison
Notes: Updates
Per. Periodic updates
Trig. Occurred based on information change
Load Balance
Multiple path & balance between equal-cost routes

## Slide 32: BGP – Operation Example
How BGP work
  The whole Internet is a graph of autonomous systems
  XZ
    Original: XABCZ
    X advertise this best path to his neighbor W
  WZ
    WXABCZ
Z
X
W

## Slide 33: BGP - Path Vector Protocol
https://nsrc.org/workshops/2016/senix-ixp/presentations/00-BGP-Introduction.pdf

## Slide 34: BGP - Definitions
Transit
  carrying traffic across a network
  (Commercially: for a fee) but in Taiwan…
Peering
  exchanging routing information and traffic
  (Commercially: between similar sized networks, and for no fee) but in Taiwan…
Default
  where to send traffic when there is no explicit match in the routing table
https://nsrc.org/workshops/2016/senix-ixp/presentations/00-BGP-Introduction.pdf
Notes: https://nsrc.org/workshops/2016/senix-ixp/presentations/00-BGP-Introduction.pdf

## Slide 35: BGP - Peering and Transit example

## Slide 36: BGP – World Wide (1)
https://en.wikipedia.org/wiki/Tier_1_network

## Slide 37: BGP – World Wide (2)
Default route
  End of full routing table
Full route
  Transit from other ISP / IXP
  789K – IPv4
  58K – IPv6
http://bgp.he.net/report/prefixes#_prefixes

## Slide 38: BGP – Full Route

## Slide 39: BGP Route Hijacking
Bad?
Good?
Neutral?

## Slide 40: BGP Route Hijacking Howto
BGP normally
  Exchange “reachability” information between each other
  Advertises the block of addresses to neighboring BGP
IF someone
  Advertise the addresses that does not belong to you
  Your neighboring BGP announce to others
BGP hijack explained
  https://www.youtube.com/watch?v=9NBv7lKrG1A

## Slide 41: BGP Route Hijacking
DDoS mitigation to clean center
BGP anycasting
  Like 168.95.1.1, 8.8.8.8, 8.8.4.4

## Slide 42: routed

## Slide 43: routed
Routing daemon
  Speak RIP (v1 and v2)
  Supplied with most every version of UNIX
  Two modes
    Server mode (-s) & Quiet mode (-q)
    Both listen for broadcast, but server will distribute their information
  routed will add its discovered routes to kernel’s routing table
  Support configuration file - /etc/gateways
    Provide static information for initial routing table