GUID Partition Table
2020 初版已完成
GUID Partition Table
jnlin(2019-2020, CC BY-SA)
? (1996-2018)

---
Topics
Topics
- Unified Extensible Firmware Interface (UEFI)
- Master Boot Record (MBR)
- GUID Partition Table (GPT)

---
Unified Extensible Firmware Interface
Unified Extensible Firmware Interface
Operating System
Legacy BIOS limitations
  - 16-bit processor mode
  - 1 MB addressable space
- Advantages
  - 32-bit/64-bit processor mode
  - Ability to boot from larger disk with a GPT
  - Flexible pre-OS environment, including network capability
  - Modular design
- Compatibility Support Module (CSM)
  - BIOS-MBR
  - BIOS-GPT
Extensible Firmware Interface
Firmware
Hardware

---
Master Boot Record (1/2)
Master Boot Record (1/2)
The Master Boot Record (MBR) is the first 512 bytes of a storage device
Offset	Length	Contents
0	446 bytes	Boot code area
446	64 bytes	Partition tables, each has 16 bytes
510	2 bytes	Boot signature (0x55AA)
128	Total

---
Master Boot Record (2/2)
Master Boot Record (2/2)
Drawbacks
  - (4 primary partitions) or (3 primary + 1 extended partitions)
    - Arbitrary number of logical partitions within the extended partition
  - The logical partition meta-data is stored in a linked-list structure
  - One byte partition type codes which leads to many collisions
  - Maximum addressable size is 2 TiB, i.e. any space beyond 2 TiB cannot be defined as a partition
    - MBR stores partition sector information using 32-bit LBA values
    - 512 bytes per sector
    - 232 * 512 bytes = 2 TiB

---
Booting Process
Booting Process
1. System initialization with firmware called BIOS
2. The BIOS looks for the bootloader on the MBR, then executes it
3. Bootloader reads the partition table
  1. Conventional Windows/DOS MBR bootloader search for one active and primary partition
  2. GRUB safely ignores this
2. Loading operating system

---
GUID Partition Table (1/9)
GUID Partition Table (1/9)
GUID stands for Globally Unique Identifier
  - Ex: 3F2504E0-4F89-41D3-9A0C-0305E82C3301
- Part of the UEFI specification
- Solves some legacy problems with MBR but also may have compatibility issues
- Can be used also on BIOS system via a protective MBR

---
GUID Partition Table (2/9)
GUID Partition Table (2/9)
Advantages
  - Filesystem-independent
  - No partition type collision because of GUIDs
  - 8 ZiB
    - GPT uses 64-bit LBA
    - 512 bytes per sector
    - 264 * 512 bytes = 8 ZiB
  - Backup header and partition table at the end of the disk
  - CRC32 checksums for header and partition table
LBA: Logical Block Address

---
GUID Partition Table (3/9)
GUID Partition Table (3/9)
GPT Scheme
  - LBA 0: Legacy MBR
  - LBA 1: GPT header
  - LBA 2~33: Partition entries
    - Up to 128 partitions
  - LBA 34~: Partitions
  - LBA -34~-1: Secondary GPT data
Kbolino is the original author of this work. It is based heavily upon an image created by Scorpiuss.

---
GUID Partition Table (4/9)
GUID Partition Table (4/9)
Legacy MBR (LBA 0)
  - A single partition type of 0xEE
  - For OSes cannot read GPT disks: Unknown type, no empty space
  - For GPT-aware OSes: check the protective MBR

---
GUID Partition Table (5/9)
GUID Partition Table (5/9)
GPT header (LBA 1)
Offset	Length	Contents
0	8 bytes	Signature ("EFI PART", 45 46 49 20 50 41 52 54)
8	4 bytes	Revision (For GPT version 1.0 (through at least UEFI version 2.3.1), the value is 00 00 01 00)
12	4 bytes	Header size in little endian (in bytes, usually 5C 00 00 00 meaning 92 bytes)
16	4 bytes	CRC32 of header (0 to header size), with this field zeroed during calculation
20	4 bytes	Reserved; must be zero
24	8 bytes	Current LBA (location of this header copy)
32	8 bytes	Backup LBA (location of the other header copy)
40	8 bytes	First usable LBA for partitions (primary partition table last LBA + 1)
48	8 bytes	Last usable LBA (secondary partition table first LBA - 1)
56	16 bytes	Disk GUID (also referred as UUID on UNIXes)
72	8 bytes	Partition entries starting LBA (always 2 in primary copy)
80	4 bytes	Number of partition entries
84	4 bytes	Size of a partition entry (usually 128)
88	4 bytes	CRC32 of partition array
92	*	Reserved; must be zeroes for the rest of the block (420 bytes for a 512-byte LBA)

---
GUID Partition Table (6/9)
GUID Partition Table (6/9)
GPT header (LBA 1)
# dd if=/dev/ada0 bs=512 count=1 skip=1 | hd
1+0 records in
1+0 records out
512 bytes transferred in 0.004644 secs (110259 bytes/sec)
00000000 45 46 49 20 50 41 52 54 00 00 01 00 5c 00 00 00 |EFI PART....\...|
00000010 b4 89 4d 11 00 00 00 00 01 00 00 00 00 00 00 00 |..M.............|
00000020 ff ff ff 01 00 00 00 00 28 00 00 00 00 00 00 00 |........(.......|
00000030 d7 ff ff 01 00 00 00 00 fa 2e 89 f8 d5 c6 ea 11 |................|
00000040 ad c5 08 00 27 9c b4 87 02 00 00 00 00 00 00 00 |....'...........|
00000050 80 00 00 00 80 00 00 00 0f 3e 88 1f 00 00 00 00 |.........>......|
00000060 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 |................|
*
00000200

---
GUID Partition Table (7/9)
GUID Partition Table (7/9)
Partition entries (LBA 2)
Offset	Length	Contents
0	16 bytes	Partition type GUID
16	16 bytes	Unique partition GUID
32	8 bytes	First LBA (little-endian)
40	8 bytes	Last LBA (inclusive, usually odd)
48	8 bytes	Attribute flags (e.g. bit 60 denotes read-only)
56	72 bytes	Partition name (36 UTF-16LE code units)
	128 bytes	Total

---
GUID Partition Table (8/9)
GUID Partition Table (8/9)
Partition type GUID
freebsd-boot	83BD6B9D-7F41-11DC-BE0B-001560B84F0F
freebsd	516E7CB4-6ECF-11D6-8FF8-00022D09712B
freebsd-swap	516E7CB5-6ECF-11D6-8FF8-00022D09712B
freebsd-ufs	516E7CB6-6ECF-11D6-8FF8-00022D09712B
freebsd-vinum	516E7CB8-6ECF-11D6-8FF8-00022D09712B
freebsd-zfs	516E7CBA-6ECF-11D6-8FF8-00022D09712B

---
GUID Partition Table (9/9)
GUID Partition Table (9/9)
Partition entries (LBA 2)
# dd if=/dev/ada0 bs=512 count=1 skip=2 | hd
1+0 records in
1+0 records out
512 bytes transferred in 0.000425 secs (1205747 bytes/sec)
00000000 9d 6b bd 83 41 7f dc 11 be 0b 00 15 60 b8 4f 0f |.k..A.......`.O.|
00000010 d1 0e 8a f8 d5 c6 ea 11 ad c5 08 00 27 9c b4 87 |............'...|
00000020 28 00 00 00 00 00 00 00 27 04 00 00 00 00 00 00 |(.......'.......|
00000030 00 00 00 00 00 00 00 00 67 00 70 00 74 00 62 00 |........g.p.t.b.|
00000040 6f 00 6f 00 74 00 30 00 00 00 00 00 00 00 00 00 |o.o.t.0.........|
00000050 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 |................|
*
00000080 b5 7c 6e 51 cf 6e d6 11 8f f8 00 02 2d 09 71 2b |.|nQ.n......-.q+|
00000090 f8 60 8f f8 d5 c6 ea 11 ad c5 08 00 27 9c b4 87 |.`..........'...|
000000a0 28 04 00 00 00 00 00 00 27 04 40 00 00 00 00 00 |(.......'.@.....|
000000b0 00 00 00 00 00 00 00 00 73 00 77 00 61 00 70 00 |........s.w.a.p.|
000000c0 30 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 |0...............|
000000d0 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 |................|
*
00000100 ba 7c 6e 51 cf 6e d6 11 8f f8 00 02 2d 09 71 2b |.|nQ.n......-.q+|
00000110 ca 38 94 f8 d5 c6 ea 11 ad c5 08 00 27 9c b4 87 |.8..........'...|
00000120 28 04 40 00 00 00 00 00 d7 ff ff 01 00 00 00 00 |(.@.............|
00000130 00 00 00 00 00 00 00 00 7a 00 66 00 73 00 30 00 |........z.f.s.0.|
00000140 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 |................|
*
00000200
freebsd-boot
freebsd-swap
freebsd-zfs